## Slide 1
Mission - IRIDIUM
The Iridium-Next Constellation
Communication Principle
Pierre-Yves Schini – ISAE-SUPAERO

## Slide 2: Introduction
UHF-VHF earth station in ISAE-SUPAERO
(Picture Isae-Supaero)
IDM-View simulation of Tolosat
Few passes
Short passes
Imposed passage times

## Slide 3: Concept
Use the Iridium-Next constellation as a relay to communicate with Tolosat
Pictures Iridium

## Slide 4: The Iridium-Next constellation Presentation
I. The Iridium-Next Constellation
Picture Iridium
66 satellites
780-Kilometer polar orbit
6 orbital planes
48 L-band beams
«4,700-Kilometer footprint area on Earth» (Iridium)

## Slide 5: The Iridium-Next constellation Coverage
I. The Iridium-Next Constellation
Iridium cover on the ground

## Slide 6: The Iridium-Next constellation Comparison
I. The Iridium-Next Constellation
Criterion | Iridium | Direct UHF/VHF
Session length | 114s | 300s
Visibility | 24,7% | 1,39% (per ground station)
Data rate | 340 bps | 9600 bps
Data transmitted per day | 7,2 Mb | 11,5 Mb

## Slide 7: Communication principle
II. Communication Principle
TM & TC
TC
TM

## Slide 8: Communication principle
Iridium Server
Iridium Satellite
Modem
Flight software
Email adress
Destination: DATA@sbd.iridium.com
Subject: IMEI number of the transceiver
Attachment: message.sbd
II. Communication Principle

## Slide 9: What is Next?
9602 Iridium-Modem lent by the CSUT
Onboard computer lent by the CSUT

## Slide 10
Thank you for your attention!