## Slide 1
Mission Analysis
Pierre Seeleuthner – ISAE

## Slide 2: Orbit Choice:
Orbital parameter | 
Semi-major axis (a) | 6478 km
Inclination (i) | 51.64°
Right Ascension of Ascending node | 105°
Period | 90 min
ISS orbit parameters

## Slide 3: Ground station
UHF/VHF ground station located in Toulouse:
Supaero’s UHF/VHF or ASTRE’s ASTRENOGS
Supaero’s UHF/VHF Ground station – ISAE-SUPAERO
3D-render Astrenogs - ASTRE

## Slide 4: Orbital Simulations
Simulations using NASA’s General Mission analysis Tool (GMAT)
Spacecraft | Spinning 2U Cubesat Cd = 2.1 Launch on 01/01/2024
Propagator | Numerical propagator Integrator: Dormant-Prince 78
Force Model | 10x10 JGM 2 gravity Moon+Sun influence MSISE90 drag model corrected with space weather files Solar radiation pressure

## Slide 5: Launch Date vs Solar Activity
2024
2019

## Slide 6: TOLOSAT’s lifespan
This plot gives you the lifespan while taking into account the uncertainty on the solar activity:
Nominal case: around 160 days
-2σ case (pretty pessimistic): around 110 days
+2σ case (pretty optimistic): around 250 days

## Slide 7: Other results
Mission duration | 160 days
Mean eclipse duration | 32 minutes
Visibility Sessions with Toulouse ground station | 3 sessions/day
Total visibility time per day | 18 minutes

## Slide 8: Other orbit possibility: Polar orbit at 500km
PROS | CONS
ISS might not be there anymore | More Expensive
We might not be selected to FYS | Longer Lifespan (almost 10 times longer)
Polar orbit is better suited for Earth Observation | Lower Resolution for the gravimetry measurements
Polar orbit allows better visibility wrt the Iridium constellation | 

## Slide 9: Thank You !
Electron Launch – Rocket Lab

## Slide 10: Eclipse duration

## Slide 11: I ran simulations on a few different launching dates (ISS orbit at 400 km)
01/01/2024
01/01/2021
01/01/2019
~600 days
~160 days
~300 days